## Slide 1: M. Spinelli, E. De Lena, M. Gatti, R. Scaccabarozzi, S. Campanari, S. Consonni, M.C. Romano – Politecnico di Milano G. Cinti – Italcementi 14th International Conference on Greenhouse Gas Control Technologies, GHGT-14 October 2018, Melbourne, Australia
Techno-economic analysis of Calcium Looping processes for low CO2 emission cement plants

## Slide 2: Summary
Why Calcium-looping in cement plants
Integration options of Calcium-looping in Cement plants
  Tail-end CaL configuration
  Integrated CaL configuration
  Key performance indicators
  Results
  Conclusions

## Slide 3: Why Calcium-Looping
Sorbent originates from CaCO3 which is a raw material for clinker production
CaO purge can be used in clinker production
CARBONATION
CaO+CO2→CaCO3
~ 650ºC
Flue gas (CO2)
CO2-lean flue gas
CaCO3
CaO
CO2-rich gas to sequestration
CaCO3
make-up
CaO purge
CALCINATION
CaCO3→CaO+CO2
~ 900ºC
Heat
O2
fuel

## Slide 4: Tail-end CaL configuration
Carbonator removes CO2 from cement plant flue gas  highly suitable for retrofit
CaO-rich purge from CaL calciner used as feed for the cement kiln
CFB CaL reactors: d50=100-250 μm
Particles for clinker production d50=10-20 μm
 CaL purge milled in the raw mill at low temperature

## Slide 5: Fluidized bed carbonator for Tail-end CaL configuration
Fluidized bed CaL process for cement plants demonstrated at CSIC and University of Stuttgart up to TRL6
The CaL design parameters for cement plant applications are in good agreement with the design parameters for power plant operation.
Arias et al., 2017. CO2 Capture by CaL at Relevant Conditions for Cement Plants: Experimental Testing in a 30 kW Pilot Plant. Ind. Eng. Chem. Res., 56, 2634–2640.
Hornberger et al., 2017. CaL for CO2 Capture in Cement Plants – Pilot Scale Test. Energy Procedia, 114, 6171–6174.

## Slide 6: Integrated CaL configuration
CaL carbonator integrated in the preheater, treats the rotary kiln gas only
CaL calciner coincides with the cement kiln pre-calciner
Calcined raw meal as CO2 sorbent in the carbonator
Sorbent has small particle size (d50=10-20 μm)  entrained flow reactors

## Slide 7: Entrained flow carbonator for integrated CaL configuration
1D carbonator modelling showed possibility of achieving high capture efficiency with solids/gas ratio of ~10 kg/Nm3.
Belite formation in calciner may cause a decrease of the sorbent CO2 carrying capacity  controlled calcination conditions needed.
Demonstration of chemistry and fluid-dynamics of the reactors in industrially relevant conditions needed
Spinelli et al., 2018. One-dimensional model of entrained-flow carbonator for CO2 capture in cement kilns by calcium looping process. Chemical Engineering Science, 191, 100-114.
Alonso et al., 2018. Capacities of Cement Raw Meals in Calcium Looping Systems. Energy & Fuels, 31, 13955–13962.
Visit the Cleanker poster!

## Slide 8: Heat recovery steam cycle
CaL process involves additional fuel consumption.
Excess heat recovered at high temperature by steam cycle.
The resulting steam cycle size is:
~70 MWe in the tail-end case
~20 MWe in the integrated case
Steam cycle parameters:
60-100 bar
460-530°C
Steam turbine ηis=76-86%
1-2 feed water heaters
 Steam cycle electric efficiency = 30-36%
Integrated CaL steam cycle

## Slide 9: Key Performance Indicators
Equivalent primary energy consumption:
Equivalent CO2 emissions:
Specific primary energy consumption:
Direct fuel consumption
Indirect fuel consumption (ηref,el = 45.9%)
Direct emissions
Indirect emissions (eref,el=262 kg/MWh)
Equivalent emissions of reference cement plant without capture
Equivalent fuel consumption of reference cement plant without capture

## Slide 10: Results: mass and energy balance
 | Cement plant w/o capture | Tail-end CaL (20% integration) | Tail-end CaL (50% integration) | Integrated CaL
Carbonator CO2 capture efficiency [%] | -- | 88.8 | 90.0 | 82.0
Total fuel consumption [MJLHV/tclk] | 3240 | 8720 | 7100 | 5440
Rotary kiln fuel consumption [MJLHV/tclk] | 1230 | 1220 | 1220 | 1150
Pre-calciner fuel consumpt. [MJLHV/tclk] | 2010 | 1550 | 850 | 4290
CaL calciner fuel consumpt. [MJLHV/tclk] | -- | 5950 | 5040 | 
ASU electric consumption [kWh/tcem] | -- | 85 | 73 | 62
CPU electric consumption [kWh/tcem] | -- | 110 | 101 | 89
Steam turbine production [kWh/tcem] | -- | 413 | 260 | 150
Other auxiliaries consumption [kWh/tcem] | 97 | 137 | 128 | 116
Net electricity consumpt. [kWhel/ tcem] | 97 | -81 | 42 | 117
Direct CO2 emissions [kgCO2/tclk] | 865 | 119 | 79 | 55
Indirect CO2 emissions [kgCO2/tclk] | 35 | -29 | 15 | 46
Equivalent CO2 emissions [kgCO2/tclk] | 900 | 90 | 94 | 101
Equivalent CO2 avoided [%] | -- | 90.0 | 89.5 | 88.8
SPECCA [MJLHV/kgCO2] | -- | 4.42 | 4.07 | 3.16
De Lena et al., 2017. Process integration of tail-end CaL in cement plants. Int J Greenh Gas Control. 67, 71-92.

## Slide 11: Results: economic analysis
De Lena et al. Techno-economic analysis of Calcium Looping processes for low CO2 emission cement plants. Submitted to Int J Greenh Gas Cont.
Cost of CO2 avoided mainly associated to Capex:

## Slide 12: Results: economic analysis
De Lena et al. Techno-economic analysis of Calcium Looping processes for low CO2 emission cement plants. Submitted to Int J Greenh Gas Cont.
Cost of cement vs. Carbon tax:
Cement kiln w/o capture
Integrated CaL plant
Tail-end CaL plant

## Slide 13: Conclusions
Ca-LOOPING PROCESS INTEGRATION OPTIONS:
Post-combustion capture configuration:
  Low uncertainty in the technical feasibility
  Very high CO2 capture expected
  Two calciners are present in the system, leading to high fuel consumptions
Integrated CaL configuration:
  High CO2 capture efficiency without modifying rotary kiln operation (no need of kiln oxyfiring).
  Higher thermal efficiency and lower fuel consumptions
  New carbonator design and fluid-dynamic regime: fluid-dynamics, heat management and sorbent performance need validation
  Competitive cost of CO2 avoided.
  We have ideas on how to reduce Capex and Opex of the integrated CaL system to be explored in Cleanker project

## Slide 14
This project has received funding from the European Union's Horizon 2020 research and innovation programme under grant agreement no 641185.
https://www.sintef.no/projectweb/cemcap/
Thank you
www.gecos.polimi.it
Contact: matteo.romano@polimi.it